## Slide 1: Plato optimization-based design
Sean Hardesty
PDE-Constrained Shape and Topology Optimization
Org. 1543, Simulation Modeling Sciences
East Cost Optimization Meeting
April 17, 2025
SAND2025-04659C

## Slide 2: Plato: optimization-based geometry design
Sierra Mechanics
Gradient-Based Optimization
Shape
Topology
Mesh
Strategy for automated design:
Quantify quality of design via simulation
Formulate a mathematical optimization problem.
What Plato allows users to do:
Orchestrate the workflow
Use gradient-based methods
Automatically compose function evaluations across software packages for
  Geometry
  Meshing
  Physics Simulation
Plato’s purpose at Sandia:
Platform for shape/topology optimization
Platform for continued research
Bread & butter: compliance min., stress-constrained mass min., mass mocks

## Slide 3: SIERRA Mechanics Overview
ATS-2
CTS-1
Focus evaluation on CTS-1
and ATS-2 platforms
Application Interfaces
Parallel Mesh Database
Third-party Libraries
Kokkos
Kokkos
Solvers
Build, Test, Exec, Deliver
Notes: Development of high-performance computing; collaboration on hardware architecture.

## Slide 4: The Nuclear Weapons program is the principal driver for Sandia’s Computational Simulation efforts
Delivery
Radiation Effects
Staging shock
Random vibration
Separation shock/ Aerodynamic Heating
Survivability
Assured Performance & Manufacturing
Assured Safety and Security
Mechanical Insult
Thermal Insult
Electromagnetic Insult
Security Components
Safe & Secure Transport
Notes: Recommend ”Command and Control” by Eric Schlosser
Explain why we are interested in modal optimization: design, mocks, fixtures.

## Slide 5: Modal Optimization
Structural dynamics FEM
Both depend on
Eigenvalue problem ( also depend on )
Differentiability
If are differentiable with respect to , and is simple, then are also differentiable.
If is repeated, may not even be continuous. Example:
  at
The “adjacent” basis can be calculated if are analytic. Gets a bit technical.
Mode Tracking
Identification of with .
Identification of with measured mode
Measurements not available everywhere
Figure from Ruiz et al., 2017
Notes: Obviously problematic to work with raw ARPACK output sorting by eigenvaules.
This talk will focus on mode tracking.

## Slide 6: Adjoint formulation ( simple)
Eigenvalue problem and mass normalization
,
Sensitivity equation being rearranged:
Objective function
Singular adjoint solves
Adjoint Equation:
Chain rule:
Notes: Eigenvalue derivative, adjoint equation depend only on same eigenvalue, eigenvector!
Need for specialized linear solver formulation.

## Slide 7: Modal Objectives
Matching Objective
Least-squares over pair of subspaces
Explicitly requires tracking
Eigenvector scaling as a least-squares problem
Least-Squares (Modal Projection Error)
C is a matrix whose columns are some subset of the computed modes
Least-squares over many modes
Ignores the eigenvalues
Normalized between 0 and 1
Tries to avoid tracking
Notes: Obviously problematic to

## Slide 8: BARC Problem
Component that experiences dynamic environment (modal measurement points highlighted)
Next level assembly
Goal: Design a base to replace the next level assembly that will cause the component to experience the same dynamic environment it would see if attached to the original next level assembly.
Solution Approach: Use optimization to generate a base that has the same modal characteristics as the original next level assembly. We will be using the MPE modal objective in the optimization.
Notes: Sean

## Slide 9: An Example Run…
In this example we are trying to match the first elastic mode of the next level assembly with the first 19 elastic modes of the current iteration.
The main behavior we are looking at here is whether it will try to introduce a ”cut” between the feet of the component.
Starting geometry
Notes: Sean

## Slide 10: Model Problem
From Day and Romero, 2004.
Why do we need an analytic solution?
Modal shape/topology optimization combines many working parts:
Re-meshing as design variables change
CAD or level-set mesh sensitivities
Finite Element approximation of the modes
Computation of the objective and gradient
 | Initial | Target | Optimized (ROL, p=2) | Optimized (ROL, p=3) | Optimized (Matlab, analytic)
 | 4.2 | 5.0 | 5.0005957 | 4.9999404 | 4.999999527709537
 | 5.0 | 6.0 | 5.998512 | 5.9999854 | 5.999999702101519
 | 6.3 | 7.0 | 7.000059 | 6.9999601 | 7.000000031488898
 | Initial | Target | Optimized (ROL, p=2) | Optimized (ROL, p=3) | Optimized (Matlab, analytic)
 | 4.2 | 5.0 | 5.0005957 | 4.9999404 | 4.999999527709537
 | 5.0 | 6.0 | 5.998512 | 5.9999854 | 5.999999702101519
 | 6.3 | 7.0 | 7.000059 | 6.9999601 | 7.000000031488898
Notes: Not all starting points converge.

## Slide 11: Matching objective (no tracking)

## Slide 12: Matching objective (greedy tracking)
Notes: “Hungarian” algorithm tracking result doesn’t look very different.

## Slide 13: Least-squares (no tracking)

## Slide 14: Least-squares (L1 regularization)

## Slide 15: Frequency optimization of cylinders
Dimensions of cylinders:
Length: 95 mm
Thickness (): 3mm, 1mm
Outer radius (): 25 mm
Middle radius:
Inextensional mode frequencies
(Lord Rayleigh, 1877, ):
Lowest mode frequency:
3mm thickness: 3510 Hz
1mm thickness: 1076 Hz

## Slide 16: Known properties of thin cylinders
Stainless Steel
100mm long, 25mm outer radius, 3mm thickness
3,460 Hz (SD, Tet10)
3,510 Hz (Lord Rayleigh)
Goal: Raise the first natural frequency while maintaining the same mass.
Notes: Sean

## Slide 17: Plato Problem Setup
1mm thick fixed outer shell
Optimizable region
Objective:
Raise natural frequency (Sierra/SD)
Match mass target
Geometry Description: Levelsets via Krino
Notes: Sean

## Slide 18: Optimized Design
Notes: Sean

## Slide 19: First Mode of Optimized Design
Frequency: 11,595 Hz
(235% increase from 3460 Hz)
Notes: Sean

## Slide 20: Performance at Frequency of Concern
Original frequency of concern: 3460 Hz
How will both the original design and the optimized design perform with a loading that would accentuate the first mode shape of the non-optimized design at the original frequency of concern?
A loading was derived based on the analytic calculation of the first mode shape of the cylinder and then applied at the 3300 Hz frequency (not right at the eigenvalue of 3460 Hz).
Unoptimized
Optimized
@ 3300 Hz:
Max displacement unoptimized: 5.43e-5
Max displacement optimized: 9.075e-7
Notes: Sean

## Slide 21: Comparison with computed values
https://www.google.com/url?sa=i&url=https%3A%2F%2Feducation.ti.com%2Fen%2F~%2Fmedia%2F41d1300939f1430a9ebb85e99d4de212.ashx%3Fh%3D16%26thn%3D1%26w%3D16%26rev%3Dce6b43e9-9ddb-48d0-8f0f-5d527196591e&psig=AOvVaw2Wbast8kM8WGBNeD9yZCnv&ust=1725036709629000&source=images&cd=vfe&opi=89978449&ved=0CBYQ3YkBahcKEwjYgefg1JqIAxUAAAAAHQAAAAAQBA
11595 Hz (F#9, SD)
11113 Hz (F9, Measured)
3510 Hz (A7, Rayleigh)
3136 Hz (G7, Measured)
1076 Hz (C#6, Rayleigh)
927 Hz (A#5, Measured)
End of standard 88-key piano keyboard